## Slide 1: Infection Prevention and Control (IPC) for Ebola or Marburg: Waste Management Part 2 - Final Waste Disposal
Healthcare Settings with Limited to Intermediate Resources
Updated: June 2026
Notes: Intended Audience: This presentation focuses on what facilities management staff should know about proper waste disposal for medical facilities during an outbreak of Ebola disease (Ebola) or Marburg virus disease (Marburg). This is the second in a two-part series on waste management. Part 1 of the Waste Management presentations focuses on the all the steps in the process of waste management while Part 2 takes an in-depth look at the final step: waste disposal. You can find Part 1 on the IPC for Ebola or Marburg web page on cdc.gov.
Please note that the training topics for IPC for Ebola or Marburg are published in sequence with the expectation that participants will progress through the series. You may, however, mix and match content to meet participant needs, and you may need to adjust the sample script accordingly.
Estimated time with audience participation: Approximately 20-25 minutes
Script:
Welcome! In the last session, we focused on an overview of the waste management process. Today we'll be taking an in-depth look at the last step in that process: final waste disposal for medical facilities during an outbreak of Ebola disease – or Ebola – or Marburg virus disease - or Marburg and how proper waste disposal can keep you and your community safe.

## Slide 2: Learning Objectives
After this presentation, participants will be able to
  Explain why proper waste disposal during an outbreak of Ebola or Marburg is important
  Identify ways to improve final waste disposal at their own facilities.
Notes: Script:
We have two learning objectives for today. By the end of our time together today, you should be able to explain why proper waste disposal during an Ebola or Marburg outbreak is important and identify ways to improve final waste disposal at your own facilities.

## Slide 3: Discuss
Once waste has been collected from the waste bins in your facility, how is waste disposed of?
Does waste disposal differ for general waste, infectious waste, or other kinds of waste collected? If so, how?
Notes: Activating background knowledge:
A key benefit of working with adult learners is that they likely already have some knowledge or experience related to the topic you are teaching. Activating background knowledge helps participants connect new learning to what they already know and may help them understand and remember new information better. It also helps you, the instructor, to identify gaps in knowledge where you may need to spend extra time or add emphasis while teaching. Use this slide as an opportunity to let participants share what they already know.
Script:
Let’s start with a question. Once waste has been collected from the waste bins in your facility, how is waste disposed of?
Does waste disposal differ for general waste, infectious waste, or other kinds of waste collected? If so, how?
[Give participants two to three minutes to share.]

## Slide 4: Waste Disposal
Notes: Script:
We are going to talk in detail today about appropriate ways to dispose of waste, and as you listen, I want you to think about how these considerations compare to your facility’s current practices.
But before we get into how to dispose of waste, let’s talk about why proper waste disposal is so important during an outbreak of Ebola or Marburg.

## Slide 5: Why Is Waste Disposal Important?
Inappropriate waste management poses potential health risks to you, your patients and other staff in your facility, as well as to your community.
Potential risks:
  Exposure to items contaminated with viruses that cause Ebola or Marburg (e.g., contaminated gloves)
  Exposure to sharp items that pose a risk of physical injury as well as exposure to viruses that cause Ebola or Marburg (e.g., used needles)
Notes: Script:
Remember from our first session on waste management that inappropriate waste management poses potential health risks to you, your patients, and other staff at your healthcare facility, as well as to your community. Potential risks might include exposure to items contaminated with viruses that cause Ebola or Marburg, such as contaminated gloves, or exposure to sharp items such as used needles that pose a risk of physical injury as well as exposure to viruses that cause Ebola or Marburg.
Knowing why waste disposal is so important at medical facilities during an outbreak of Ebola or Marburg, let’s get into the details of how to dispose of waste safely.

## Slide 6: Waste Disposal
Healthcare facilities must have a functional system for the final disposal of waste
Infectious and potentially infectious waste must be:
  Incinerated
  OR
  Treated with non-burn treatment (autoclaving/grinding or other alternative treatment) before being placed in regular waste stream
  OR
  Buried
Notes: Script:
To review from our last training, every facility must have a functional device for the final disposal of waste including an incinerator with ash pit or a non-burn system such as an autoclaving and grinding process for infectious waste. If infectious waste is autoclaved and grinded, it can be then added to the regular waste stream for landfill disposal.
In some very low-resource settings, a temporary burning pit may also be an option for treating and then burying infectious waste on-site while longer term improvements are being made. It is also common to have a placenta or organic waste pit on site, as other methods of treatment for these may not be culturally acceptable.

## Slide 7: Incinerator Placement
On the healthcare facility property
Away from flow of patients
In an area where they will NOT disturb people
Notes: Script:
Now, let’s talk about incinerating waste. Incinerators should be located on the healthcare facility property, away from the flow of patients, and in an area where they will not disturb people. This means that they should be in a place as far away from patients, visitors, and community members as possible.

## Slide 8: Incinerators Options
Best Option
Not Recommended
High temperature incinerators
De Montfort brick (double-chamber) incinerators
  Allows for higher temperatures = more effective waste incineration and reduced toxic emissions
Drum incinerators (not recommended)
  A better option than open burning
Notes: Script:
Different types of incinerators may be available at your facility. The best incinerators for disposing of waste during an outbreak of Ebola or Marburg are high temperature incinerators. Higher temperatures allow for more effective waste incineration and reduced toxic emissions.
If a high temperature incinerator is not available, the next best option is a de Montfort brick double-chamber incinerator (pictured). Compared to single-chamber incinerators, de Montfort brick incinerators allow for higher temperatures.
Drum incinerators are not recommended for disposing of waste during an outbreak of Ebola or Marburg, but if they are all that is available, they are a better option than open burning in a burning pit.
Sometimes facilities have incinerators, but they’re not functioning because they need maintenance. This leads to waste piling up, which is something we want to avoid. So, not just having an incinerator, but having a functional incinerator is very important.

## Slide 9: Interim Option: Burn Pits
Generally, it is best to avoid open burning of healthcare waste
  releases toxic gases
  does not reach high enough temperatures to fully destroy infectious waste
In emergencies, burn pits can be used until incinerators or other treatment methods (such as autoclaves) become available.
Notes: Script:
It’s generally best to avoid open burning of healthcare waste because it can release toxic gases and does not reach a high enough temperature to fully destroy infectious waste. However, in emergencies, burn pits can be used until incinerators or other treatment methods such as autoclaves become available.

## Slide 10: Interim Option: Burn Pits (continued)
Burn pits should be
  away from patient flow
  dug deep
  marked off
Notes: Script:
If your facility has to use a burn pit to dispose of medical waste, it should meet certain requirements. As with incinerators, burn pits should be located
On the healthcare facility property,
Away from the flow of patients,
And in an area where they will NOT attract people.
They should be dug deep and marked off. Particularly in the context of Ebola or Marburg, we don’t want burn pits being in a place where people might come to sift through to see if they can find anything useful.
These pictures are good examples of what safe burn pits can look like.

## Slide 11: Other Considerations
Avoid situations where:
  Waste isn’t segregated
  Waste is overflowing because the final disposal option needs maintenance
Notes: Script:
We want to avoid situations such as what you see here, where waste isn’t segregated or where it’s overflowing because the final disposal option needs maintenance.

## Slide 12: Knowledge Check: Waste Disposal
While visiting a healthcare facility, you observe this example of waste disposal.
What suggestions could you give?
Notes: Script:
Now that we’ve talked about proper waste disposal, let’s put that knowledge to work. Imagine that you are visiting a healthcare facility, and you observe this example of waste disposal. What suggestions could you give to help make waste disposal safer at this facility?
[Allow a few minutes for discussion. Possible answers are on the next slide.]

## Slide 13: Knowledge Check: Feedback
Assist the facility to identify solutions to deal with current load of waste
  Use an incinerator if available.
  If no incinerator available, dig sufficiently wide and deep burn pit
  Carefully and safely (wearing appropriate PPE and using a shovel) transfer waste to burn pit and burn in sections
Notes: [You may wish to adapt this script based on what participants discussed on the previous slide.]
Script:
This facility needs some assistance identifying solutions to deal with current waste load. They should be using an incinerator if it’s available. If they have no incinerator available, their burn pit needs to be sufficiently wide and deep and should be marked off so that people won’t enter either intentionally or unintentionally.
After they have constructed a sufficient burn pit, they will need to move this waste to the burn pit. To do so safely and carefully, they would need to use a shovel for this task and wear appropriate PPE, which includes heavy duty gloves, gown or coveralls, face mask, eye protection, and foot covers or boots. They should transfer the waste in sections and burn each section.

## Slide 14: Reflection
Where is final waste disposal at your facility?
What maintenance might be needed?
Is there capacity to take on additional waste (e.g., isolation units, additional PPE waste)?
What resources, such as fuel for burning waste and transporting equipment, might be needed?
Notes: Reflection:
Encourages participants to apply, analyze, and/or evaluate what they have learned, which helps them to deepen their understanding of the topic
Allows participants to think about how they’re new learning applies to their previous knowledge or experiences, which helps them better understand and remember the ideas taught
Allows you to check participants’ comprehension of what has been discussed to see if any topics need to be reviewed
This exercise might be performed differently depending on who your audience is. If only one person per facility is in attendance, this discussion could be done in small groups with time for sharing with the large group afterwards or as a whole-group discussion (depending on the size of the group and time available). If the audience consists of several members each from different facilities, you might give them time to discuss with the others from their facility and then share as a large group afterwards. Allow about 10 minutes for discussion if possible.
Script:
Let’s think now about how waste disposal happens at your facility and about how the facility’s waste disposal could be improved for safer functioning during an outbreak of Ebola or Marburg.
First, where is the final waste disposal at your facility. Is it on-site or off-site?
If it’s on-site
Does it meet the requirements of being far from the flow of patients and being in an area that won’t disturb people?
  If not, what could be changed to help it meet these requirements?
Is there maintenance needed? If so, what kinds of maintenance? What resources would be needed for this?
Is there capacity to take on additional waste, for example, if an isolation unit is set up?
What resources, such as fuel for burning waste and transport equipment such as a wheelbarrow, might be needed for the waste management process at your facility?
If final waste disposal is off-site, what resources might be needed to help facilitate the waste disposal process?

## Slide 15: Key Takeaways
Proper medical waste disposal during an outbreak of Ebola or Marburg is crucial to keep you, others at your facility, and your community safe.
A high temperature incinerator is the best option for incinerating medical waste.
If a burn pit must be used as an interim option, it should be away from patient flow, dug deep, and marked off.
Notes: Script:
As we conclude for today, there are some key things I hope you’ll take away from today’s session:
First, proper medical waste disposal during an outbreak of Ebola or Marburg is crucial to keep you and your community safe.
When it comes to waste disposal in the context of Ebola or Marburg, a high temperature incinerator is the best option for incinerating medical waste, but if a burn pit must be used as an interim option, it should be away from patient flow, dug deep, and marked off.

## Slide 16: Thank you!